## Slide 1
Yangyang Fu, PhD
Texas A&M University
8/30/2021
Introduction to an Equation-based Object-oriented Modeling Language: Modelica

## Slide 2: Agenda
A Simple Differential Algebraic Equation (DAE)
Modelica/Dymola
Introduction to Modelica by Examples
Your First Modelica Model
Revisit Some Modelica Basics

## Slide 3: A Simple DAE
% call matlab ode solver to solve
tspan = [0, 10];
x0 = 1;
[t,x] = ode45(@SimpleDAE, tspan, x0);
% define DAE system in terms of ODE format
function dx=SimpleDAE(t, x)
y = sqrt(x^2-1);
dx = (1- y)/2;
end
Arrange to
ODE
Matlab Implementation
Take the arranged format
Take the format AS IT IS
Modelica Implementation
model SimpleDAE
Real x(start=1);
Real y;
equation
2*der(x) = 1 - y;
x^2 - y^2 = 1;
annotation (experiment(
StartTime=0,
StopTime=10,
__Dymola_Algorithm="Dassl”
));
end SimpleDAE;

## Slide 4: Modelica
What is Modelica?
How to Build a Modelica Model

## Slide 5: Modelica Modeling and Simulation Procedure
Modeling
Compilation
Simulation

## Slide 6: Dymola
Dymola is a commercial tools for performing Modelica modeling and simulation
Some others:
  OpenModelica – opensource
  jModelica – opensource/commercial
  Simulation X
  MapleSim
  …

## Slide 7: Dymola Interfaces
Run a “helloworld” example
Tour Dymola

## Slide 8: Introduction to Modelica by Examples
Modeling with Modelica
An Electrical System Example
A Mechanical System Example
A Thermal System Example

## Slide 9: Modeling with Modelica
Flat and hierarchical models
  data types, attributes, components, interface-variables, package concept, inheritance
Special model classes
  constraints on variables and parameters
    input, output, final, protected
  equation vs algorithm
  class types in Modelica
    type, connector, model, block, function, package
Matrices, arrays and arrays of components
  definition, index sets, for-in-loop, array functions
Physical fields
  global variables
Hybrid modeling
  events, if-then-else, when-statement

## Slide 10: An Electrical Example
Low-Pass RLC Filter
Mathematical Representation
Knowns:
Unknowns:
4 unknowns with 4 equations
V?

## Slide 11: A Straight-forward Way – Flat Model
model RLC1 "A low-pass RLC filter example using text editor"
type Voltage=Real(unit="V");
type Current=Real(unit="A");
type Resistance=Real(unit="Ohm");
type Capacitance=Real(unit="F");
type Inductance=Real(unit="H");
parameter Voltage Vb=24 "Battery voltage";
parameter Inductance L = 1;
parameter Resistance R = 100;
parameter Capacitance C = 1e-3;
Voltage V;
Current i_L;
Current i_R;
Current i_C;
equation
V = i_R*R;
C*der(V) = i_C;
L*der(i_L) = (Vb-V);
i_L=i_R+i_C;
annotation (experiment(StartTime=0,
StopTime=2,
__Dymola_Algorithm="Dassl"));
end RLC1;
Define a model RLC1 and provide descriptive documentation

## Slide 12: A Straight-forward Way – Flat Model
model RLC1 "A low-pass RLC filter example using text editor"
type Voltage=Real(unit="V");
type Current=Real(unit="A");
type Resistance=Real(unit="Ohm");
type Capacitance=Real(unit="F");
type Inductance=Real(unit="H");
parameter Voltage Vb=24 "Battery voltage";
parameter Inductance L = 1;
parameter Resistance R = 100;
parameter Capacitance C = 1e-3;
Voltage V;
Current i_L;
Current i_R;
Current i_C;
equation
V = i_R*R;
C*der(V) = i_C;
L*der(i_L) = (Vb-V);
i_L=i_R+i_C;
annotation (experiment(StartTime=0,
StopTime=2,
__Dymola_Algorithm="Dassl"));
end RLC1;
Define different unit classes by using type

## Slide 13: A Straight-forward Way – Flat Model
model RLC1 "A low-pass RLC filter example using text editor"
type Voltage=Real(unit="V");
type Current=Real(unit="A");
type Resistance=Real(unit="Ohm");
type Capacitance=Real(unit="F");
type Inductance=Real(unit="H");
parameter Voltage Vb=24 "Battery voltage";
parameter Inductance L = 1;
parameter Resistance R = 100;
parameter Capacitance C = 1e-3;
Voltage V;
Current i_L;
Current i_R;
Current i_C;
equation
V = i_R*R;
C*der(V) = i_C;
L*der(i_L) = (Vb-V);
i_L=i_R+i_C;
annotation (experiment(StartTime=0,
StopTime=2,
__Dymola_Algorithm="Dassl"));
end RLC1;
Define model parameters (usually represent physical sizes etc)
Parameter is changeable before simulation, but is not changeable during simulation
Modelica Declaration
prefix
class
instance
parameter Voltage Vb=24 "Battery voltage";
descriptive doc (optional)

## Slide 14: A Straight-forward Way – Flat Model
model RLC1 "A low-pass RLC filter example using text editor"
type Voltage=Real(unit="V");
type Current=Real(unit="A");
type Resistance=Real(unit="Ohm");
type Capacitance=Real(unit="F");
type Inductance=Real(unit="H");
parameter Voltage Vb=24 "Battery voltage";
parameter Inductance L = 1;
parameter Resistance R = 100;
parameter Capacitance C = 1e-3;
Voltage V;
Current i_L;
Current i_R;
Current i_C;
equation
V = i_R*R;
C*der(V) = i_C;
L*der(i_L) = (Vb-V);
i_L=i_R+i_C;
annotation (experiment(StartTime=0,
StopTime=2,
__Dymola_Algorithm="Dassl"));
end RLC1;
Define model variables representing unknowns.
Variable is changeable during simulation, and dependent on other variables or parameters.

## Slide 15: A Straight-forward Way – Flat Model
model RLC1 "A low-pass RLC filter example using text editor"
type Voltage=Real(unit="V");
type Current=Real(unit="A");
type Resistance=Real(unit="Ohm");
type Capacitance=Real(unit="F");
type Inductance=Real(unit="H");
parameter Voltage Vb=24 "Battery voltage";
parameter Inductance L = 1;
parameter Resistance R = 100;
parameter Capacitance C = 1e-3;
Voltage V;
Current i_L;
Current i_R;
Current i_C;
equation
V = i_R*R;
C*der(V) = i_C;
L*der(i_L) = (Vb-V);
i_L=i_R+i_C;
annotation (experiment(StartTime=0,
StopTime=2,
__Dymola_Algorithm="Dassl"));
end RLC1;
Define model equations based on physical laws.
Resistor
Capacitor
Inductor
Current Law

## Slide 16: A Straight-forward Way – Flat Model
model RLC1 "A low-pass RLC filter example using text editor"
type Voltage=Real(unit="V");
type Current=Real(unit="A");
type Resistance=Real(unit="Ohm");
type Capacitance=Real(unit="F");
type Inductance=Real(unit="H");
parameter Voltage Vb=24 "Battery voltage";
parameter Inductance L = 1;
parameter Resistance R = 100;
parameter Capacitance C = 1e-3;
Voltage V;
Current i_L;
Current i_R;
Current i_C;
equation
V = i_R*R;
C*der(V) = i_C;
L*der(i_L) = (Vb-V);
i_L=i_R+i_C;
annotation (experiment(StartTime=0,
StopTime=2,
__Dymola_Algorithm="Dassl"));
end RLC1;
Define others, e.g., experiment setup

## Slide 17: A “Modelica” Way – Hierarchical Model
model RLC2 "A low pass RLC filter using graphical editor"
parameter Modelica.SIunits.Inductance L=1;
parameter Modelica.SIunits.Resistance R=100;
parameter Modelica.SIunits.Voltage Vb=24 “Battery voltage";
parameter Modelica.SIunits.Capacitance C=1e-03
Modelica.Electrical.Analog.Basic.Inductor inductor(L=L);
Modelica.Electrical.Analog.Basic.Resistor resistor(R=R);
Modelica.Electrical.Analog.Basic.Capacitor capacitor(C=C);
Modelica.Electrical.Analog.Sources.ConstantVoltage battery(V=Vb);
Modelica.Electrical.Analog.Basic.Ground ground;
equation
connect(resistor.n, battery.p);
connect(capacitor.n, battery.p);
connect(battery.p, ground.p);
connect(battery.n, inductor.p);
connect(capacitor.p, inductor.n);
connect(inductor.n, resistor.p);
annotation (experiment(StartTime=0,
StopTime=2,
__Dymola_Algorithm="Dassl"));
end RLC2;
Direct Representation
Direct Representation with Virtual Sensors
RLC2
RLC2WithSensors
Source Code

## Slide 18: Source Code Comparison
model RLC1
type Voltage=Real(unit="V");
type Current=Real(unit="A");
type Resistance=Real(unit="Ohm");
type Capacitance=Real(unit="F");
type Inductance=Real(unit="H");
parameter Voltage Vb=24 "Battery voltage";
parameter Inductance L=1;
parameter Resistance R=100;
parameter Capacitance C=1e-3;
Voltage V;
Current i_L;
Current i_R;
Current i_C;
equation
L*der(i_L) = (Vb-V);
V = i_R*R;
C*der(V) = i_C;
i_L=i_R+i_C;
annotation (experiment(StartTime=0,
StopTime=2,
__Dymola_Algorithm="Dassl"));
end RLC1;
model RLC2
parameter Modelica.SIunits.Voltage Vb=24 “Battery voltage";
parameter Modelica.SIunits.Inductance L=1;
parameter Modelica.SIunits.Resistance R=100;
parameter Modelica.SIunits.Capacitance C=1e-03
Modelica.Electrical.Analog.Basic.Inductor inductor(L=L);
Modelica.Electrical.Analog.Basic.Resistor resistor(R=R);
Modelica.Electrical.Analog.Basic.Capacitor capacitor(C=C);
Modelica.Electrical.Analog.Sources.ConstantVoltage battery(V=Vb);
Modelica.Electrical.Analog.Basic.Ground ground;
equation
connect(resistor.n, battery.p);
connect(capacitor.n, battery.p);
connect(battery.p, ground.p);
connect(battery.n, inductor.p);
connect(capacitor.p, inductor.n);
connect(inductor.n, resistor.p);
annotation (experiment(StartTime=0,
StopTime=2,
__Dymola_Algorithm="Dassl"));
end RLC2;

## Slide 19: Questions
Plot and compare V from RLC1 and RLC2?
  Plot V from RLC1 after simulation
  Plot V.v from RLC2WithSensors after simulation
Difference between flat modeling and hierarchical modeling?
  Flat modeling requires mathematical representation – difficult for complex system
  Hierarchical modeling requires physical representation – easy for complex system
How does the keyword “connect” formulate the equations?
  Acausal connections – connector
  Causal connections – signal

## Slide 20: Component Model
Component 1
Component 2
acausal connector
causal connector
causal connection
acausal connection
A component class should be defined independently of the environment, very essential for reusability
A component may internally consist of other components, i.e. hierarchical modeling
Complex systems usually consist of large numbers of connected components

## Slide 21: Acausal Connection – Acausal Connector
Electrical
R1
R3
R2
Two kinds of variables in acausal connectors
Potential variable: Connected variables are identical;
Flow variable: connected variables fulfil the zero-sum equation
v
+
i
pin
connector Pin
SI.ElectricPotential v;
flow SI.Current i;
end Pin;
Pin pin;
connector class
instance name of connector class
potential variable class name
flow variable class name
an instance pin of class Pin

## Slide 22: Acausal Connection – Acausal Connector
Electrical
R1
R3
R2
connect(R1.p,R2.p);
connect(R1.p,R3.p);
connect(R2.p,R3.p);
connector Pin
SI.ElectricPotential v;
flow SI.Current i;
end Pin;

## Slide 23: Other Acausal Connectors
Other physical acausal connector classes in Modelica Standard Library
Domain Type | Potential | Flow | Modelica Library
Electrical | Voltage | Current | Electrical.Analog
Translational | Position | Force | Mechanics.Translational
Rotational | Angle | Torque | Mechanics.Rotational
Magnetic | Magnetic potential | Magnetic flux | Magnetic.FluxTubes
Hydraulic | Pressure | Volume/mass flow | Fluid
Thermal | Temperature | Heat flow | Thermal.HeatTransfer
connector XXX
Potential variable_name;
flow Flow variable_name;
end XXX;

## Slide 24: Causal Connection – Causal Connector
connector InPort
input Real signal_name;
end InPort;
connector OutPort
output Real signal_name;
end OutPort;
fixed causality
PID Controller Class
input signal: instance of InPort
output signal: instance of OutPort

## Slide 25: Common Component Structure
p
n
+
-
TwoPin
partial model TwoPin
SI.Voltage v ;
SI.Current i ;
Pin p ;
Pin n ;
equation
v = p.v - n.v;
0 = p.i + n.i;
i = p.i;
end TwoPin;
// TwoPin is the same as OnePort in
// Modelica.Electrical.Analog.Interfaces
connector Pin
SI.ElectricPotential v;
flow SI.Current i;
end Pin;
partial class (cannot be instantiated)
positive pin
negative pin
The base class TwoPin has two connectors p and n for positive and negative pins.
Can this model be solved with the given equations and inputs ()?
No. There are only 3 equations for 4 unknowns ().

## Slide 26: Electrical Components
model Resistor “Ideal electrical resistor”
extends TwoPin;
parameter Real R “Resistance”;
equation
R*i = v;
end Resistor;
model Inductor “Ideal electrical inductor”
extends TwoPin;
parameter Real L “Inductance”;
equation
L*der(i) = v;
end Inductor;
model Capacitor “Ideal electrical capacitor”
extends TwoPin;
parameter Real C “Capacitance”;
equation
i = C*der(v);
end Capacitor;
p
n
+
-
p
n
+
-
p
n
+
-

## Slide 27: Revisit RLC2
model RLC2 "A low pass RLC filter using graphical editor"
parameter Modelica.SIunits.Inductance L=1;
parameter Modelica.SIunits.Resistance R=100;
parameter Modelica.SIunits.Voltage Vb=24 “Battery voltage";
parameter Modelica.SIunits.Capacitance C=1e-03
Modelica.Electrical.Analog.Basic.Inductor inductor(L=L);
Modelica.Electrical.Analog.Basic.Resistor resistor(R=R);
Modelica.Electrical.Analog.Basic.Capacitor capacitor(C=C);
Modelica.Electrical.Analog.Sources.ConstantVoltage battery(V=Vb);
Modelica.Electrical.Analog.Basic.Ground ground;
equation
connect(resistor.n, battery.p);
connect(capacitor.n, battery.p);
connect(battery.p, ground.p);
connect(battery.n, inductor.p);
connect(capacitor.p, inductor.n);
connect(inductor.n, resistor.p);
annotation (experiment(StartTime=0,
StopTime=2,
__Dymola_Algorithm="Dassl"));
end RLC2;

## Slide 28: A Mechanical Example
Initial Conditions:
model Example1
type Angle=Real(unit="rad");
type AngularVelocity=Real(unit="rad/s");
type Inertia=Real(unit="kg.m2");
type Stiffness=Real(unit="N.m/rad");
type Damping=Real(unit="N.m.s/rad");
parameter Inertia J1=0.4 "Moment of inertia for inertia 1";
parameter Inertia J2=1.0 "Moment of inertia for inertia 2";
parameter Stiffness c1=11 "Spring constant for spring 1";
parameter Stiffness c2=5 "Spring constant for spring 2";
parameter Damping d1=0.2 "Damping for damper 1";
parameter Damping d2=1.0 "Damping for damper 2";
Angle phi1 "Angle for inertia 1";
Angle phi2 "Angle for inertia 2";
AngularVelocity omega1 "Velocity of inertia 1";
AngularVelocity omega2 "Velocity of inertia 2";
initial equation
phi1 = 0;
phi2 = 1;
omega1 = 0;
omega2 = 0;
equation
// Equations for inertia 1
omega1 = der(phi1);
J1*der(omega1) = c1*(phi2-phi1)+d1*der(phi2-phi1);
// Equations for inertia 2
omega2 = der(phi2);
J2*der(omega2) = c1*(phi1-phi2)+d1*der(phi1-phi2)-c2*phi2-d2*der(phi2);
annotation (experiment(StopTime=5, __Dymola_Algorithm="Dassl"));
end Example1;

## Slide 29: A Thermal Example
model Example1
parameter Real T_inf=25 "Ambient temperature";
parameter Real T0=90 "Initial temperature";
parameter Real h=0.7 "Convective cooling coefficient";
parameter Real A=1.0 "Surface area";
parameter Real m=0.1 "Mass of thermal capacitance";
parameter Real c_p=1.2 "Specific heat";
Real T "Temperature";
initial equation
T = T0 "Specify initial value for T";
equation
m*c_p*der(T) = h*A*(T_inf-T)"Newton's law of cooling";
end Example1;
Newton Cooling:
Flat Math Model:
Hierarchical Physical Model:

## Slide 30: Your First Modelica Model
We want to control the rotational speed of an outgoing shaft at a given speed reference.
The studied system diagram is shown in the figure.
Proposed Steps
  Step 0: Configure model/package structure
  Step 1: Build a DC-motor model
  Step 2: Build a DC-motor with mechanical rotational devices
  Step 3: Build a closed-loop control for the motor-driven rotational system by regulating motor voltage
Motor
Gearbox
Load
Controller
reference
rotation speed
voltage

## Slide 31: Step 1: DC-Motor Model
A Ideal DC-Motor Model
  Understand the dc motor model assumptions
  Build a dc-motor model
    Inside Motor package, create a new model and name it as DCMotor
    In the graphic editor of DCMotor, drag&drop the following components:
      Causal interface Vb: Modelica.Blocks.Interfaces.RealInput
      Acausal interface flange: Modelica.Mechanics.Rotational.Interfaces.Flange_b
      Resistor Ra: Modelica.Electrical.Analog.Basic.Resistor
      Inductor La: Modelica.Electrical.Analog.Basic.Inductor
      EMF emf: Modelica.Electrical.Analog.Basic.EMF
      Inertia inertia: Modelica.Mechanics.Rotational.Components.Inertia
      DC source with voltage input Vs: Modelica.Electrical.Analog.Sources.SignalVoltage
      Ground G: Modelica.Electrical.Analog.Basic.Ground
    Connect each component in the graphic editor – be careful about the positive/negative pins
Vb

## Slide 32: Step 1: DC-Motor Model
A Ideal DC-Motor Model
  Build a dc-motor model
    Inside Motor package, create a new model and name it as DCMotor
    In the graphic editor of DCMotor, drag&drop the following components:
    Connect each component in the graphic editor
    Propagate component parameters to the top level
      Define R in Ra
        i) Left click Ra twice, which opens a tab showing different parameters used by Ra, and locate the parameter R that to be propagated
        ii) Left click the small trangle symbol at the right of the input box, which pops a new window
        iii) In the tab window, select Propogate, choose “OK” for all popped tabs and exit.
parameter Modelica.SIunits.Resistance R "Resistance at temperature T_ref";
Modelica.Electrical.Analog.Basic.Resistor Ra(R=R)
The source code changes after propagation:

## Slide 33: Step 1: DC-Motor Model
A Ideal DC-Motor Model
  Understand the dc motor model assumptions
  Build a dc-motor model
  Connect each component in the graphic editor
  Propagate component parameters to the top level
    Define R in Ra
    Define L in La, k in emf, J in inertia
  Check your model – on the graphics mode, click “Check”
    Find and fix errors ASAP before you use it for simulation
  Make some beautiful icons if you need – In Graphics, click Icon, and start to design

## Slide 34: Step 2: DC-motor with Rotation System
Inside MotorDriveControlExample package, create a new partial model, and name it as MotorRotation
In the Graphics/Diagram, drag&drop the following components:
  A motor motor: MotorDriveControlExample.Motor.DCMotor
  A grearbox gearbox: Modelica.Mechanics.Rotational.Components.IdealGear
  A mechanical load load: Modelica.Mechanics.Rotational.Components.Inertia
  A rotation speed sensor speedSensor: Modelica.Mechanics.Rotational.Sensors.SpeedSensor
Connect them in a physical way
Assign values to key parameters
  motor:
  gearbox:
  load:
Check your model

## Slide 35: Step 3: Control Rotation System
Inside MotorDriveControlExample package, create a new model, and name it as MotorRotationControl, extending from MotorDriveControlExample.MotorRotation
In the Graphics/Diagram, drag&drop the following components:
  A referece ref: Modelica.Blocks.Sources.Step
  A feedback error: Modelica.Blocks.Math.Feedback
  A PID controller PID: Modelica.Blocks.Continuous.PID
Connect them in a physical way
  connect (speedSensor.w, error.u2)
  connect (ref.y, error.u1)
Assign values to key parameters, and check the model
  ref:
  PID:

## Slide 36: Step 3: Control Rotation System
Simulate MotorRotationControl
  Go to Simulation/Setup
    Set start time to 0, stop time to 1200 s
    Click OK and exit
  Click Simulation/Simulate to simulate model. Simulation results will be ready for plotting.
Plot response
  In the Variable Browser tab, find and plot:
    ref.y – reference speed
    speedSensor.w – measured speed

## Slide 37: Revisit Some Basics
Flat and hierarchical models
  data types, attributes, components, interface-variables, package concept, inheritance
Special model classes
  class types in Modelica
    type, connector, model, package